## Slide 1: Computer Network & Network Reference Model

## Slide 2: Computer Network & Network Reference Model
Overview of Computer Network
OSI Reference Model
TCP/IP Model
Network Topology
Network Devices

## Slide 3: Networks
Companies created networks
  As companies expanded, the need for connecting networks at different sites became very important
What is a network ?
  A network is an intricately connected system of objects, devices, or people

## Slide 4
Data Networks Classifications
LAN( Local Area Networks )
WAN( Wide Area Networks )
Node
Link

## Slide 5
LAN/WAN
Local Area Networks (LANs)
  Operate locally (cover small areas)
  Multi-user access
  High speeds expected (up to Gbps/10Gbps)
  Error rate is easily controlled
Wide Area Networks (WANs)
  Operate over larger areas
  Access over serial links, optical links, etc.
  Traditionally, have Lower speeds
  Error rate can not be easily controlled

## Slide 6: Internet
internet:
  A network whose nodes are networks
Internet
  The largest, open, interconnected computer network in the world.
  TCP/IP is the reference model of Internet
  Evolved from ARPANET
Internet

## Slide 7: Internet with Multi-layer ISP structure
Internet Service Providers (ISP)
User
Internet
ISP1
ISP2
ISP

## Slide 8
一级 ISP
一级 ISP
第一层 ISP
大公司
本地 ISP
大公司
大公司
公司
本地 ISP
本地 ISP
校园网
校园网
校园网
校园网
第二层 ISP
第二层 ISP
NAP
NAP
A
B
主机A → 本地 ISP → 第二层 ISP → NAP → 第一层 ISP → NAP → 第二层 ISP → 本地 ISP → 主机B
第一层 ISP
第二层 ISP
本地 ISP
本地 ISP
本地 ISP
本地 ISP
第一层 ISP
第一层
第二层
第三层
本地 ISP
第二层 ISP
本地 ISP
本地 ISP
本地 ISP
本地 ISP
第二层 ISP
本地 ISP
本地 ISP
第二层 ISP
Internet with Multi-layer ISP structure

## Slide 9
LAN Devices
Multiport repeater, connects PCs; Repeats signals
LAN segmentation; MAC addresses.
Hub
Bridge
Switch
Router
Multiport-bridge; Full bandwidth
Path determination; Packet switching

## Slide 10
Modem
CSU/DSU
TA/NT1
Analog to Digital;
Remote LAN connections
Router
Path determination; Packet switching
WAN Devices

## Slide 11
LAN service: Ethernet, the most popular service
WAN services...
  Modem
  ISDN
  DSL
  Frame Relay
  ATM
  T1/E1
  T3
  STS-1, STS-3, STS-48 (SONET/SDH)
LAN Services and WAN Services

## Slide 12
Data
Data is sent in bits, 1s and 0s.
Data is not the information itself
Data is an encoded form of information which is a series of electrical impulses/optical signals into which information is transmitted for sending

## Slide 13: Protocol
It is possible for different types of computer systems to communicate
All devices must speak the same “language” or use the same protocol (use same set of rules).

## Slide 14
Data Packets
For transmission, computer data is often broken into small, easily transmitted units
  Using the OSI model, these units can be called packets, or frames or segments
Why data packets?
  Computers can take turns sending packets
  If packet is lost, only small amount of data must be retransmitted.
  Data can take different paths.

## Slide 15
Source and Destination
  Source address specifies the identity of the computer sending the packet.
  Destination address specifies the identity of the computer designated to receive the packet.

## Slide 16
Media Types
AIR
carries light, radio, microwave
Media—material through which data packets travel

## Slide 17
Digital Bandwidth
Bandwidth is the measure of how much information can flow from one place to another in a given amount of time.
Measured in: bits/second (bps)

## Slide 18
Throughput  Bandwidth
Throughput
Actual, measured, bandwidth, at a specific time

## Slide 19: Computer Network & Network Reference Model
Overview of Computer Network
OSI Reference Model
TCP/IP Model
Network Topology
Network Devices

## Slide 20
OSI (Open System Interconnection) Model
Proposed by International Organization for Standardization (ISO)
A network model that help network builders implement networks that could communicate and work together
Describes how information or data moves from one computer through a network to another computer
a layered communication process
  Each layer performs a specific task

## Slide 21
The OSI Reference Model
User interface
Data presentation and encryption
Inter-host connection
End-to-end connections
Addresses and best path
Access to media
Binary transmission
Each layer has a unique function.
7
6
5
4
3
2
1
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 22
Why a Layered Model?
Reduce Complexity
Standardizes interfaces
Facilitates modular engineering
Ensures interoperable technology
Accelerates evolution
Simplifies teaching and learning

## Slide 23
The OSI Reference Model
The top 3 layers are known as the application layers
  because they deal with the user interface, data formatting, and the application access.
Application
Presentation
Session

## Slide 24
The OSI Reference Model
Layers 1-4 are known as the data flow layers
  because they control the physical delivery of messages over the network.
4
3
2
1
Transport
Network
Data Link
Physical

## Slide 25
Keywords: Signal and Media
User interface
Data presentation and encryption
Inter-host connection
End-to-end connections
Addresses and best path
Access to media
Binary transmission
Application
Presentation
Session
Transport
Network
Data Link
Physical
7
6
5
4
3
2
1
Layer 1: The Physical Layer
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 26
defines the electrical and functional specifications for the link between end systems (including media)
defines voltage levels, timing of voltage changes, physical data rates, maximum transmission distances, physical connectors, and other, similar attributes
Layer 1: The Physical Layer

## Slide 27
Keywords: frame, media access control
User interface
Data presentation and encryption
Inter-host connection
End-to-end connections
Addresses and best path
Access to media
Binary transmission
Application
Presentation
Session
Transport
Network
Data Link
Physical
7
6
5
4
3
2
1
Layer 2: The Data Link Layer
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 28
provides reliable transit of data across a physical link
is concerned with physical (as opposed to logical) addressing, network topology, network access, error notification, ordered delivery of frames, and flow control
Layer 2: The Data Link Layer

## Slide 29
Keywords: Path selection, Routing, Addressing
User interface
Data presentation and encryption
Inter-host connection
End-to-end connections
Addresses and best path
Access to media
Binary transmission
Application
Presentation
Session
Transport
Network
Data Link
Physical
7
6
5
4
3
2
1
Layer 3: The Network Layer
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 30
Layer 3: The Network Layer
Provide connectivity and path selection between two end systems where routing occurs
These may be located on geographically separated networks

## Slide 31
User interface
Data presentation and encryption
Inter-host connection
End-to-end connections
Addresses and best path
Access to media
Binary transmission
Application
Presentation
Session
Transport
Network
Data Link
Physical
7
6
5
4
3
2
1
Keywords: Reliability, Flow control, Error correction
Layer 4: The Transport Layer
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 32
Layer 4: The Transport Layer
segments and reassembles data into a data stream
concerned with how reliable transport over an internetwork is accomplished
responsible for reliable network communication between end nodes and provides mechanisms for the establishment, maintenance, and termination of virtual circuits, transport fault detection and recovery, and information flow control

## Slide 33
Keywords: Dialog and Conversations
User interface
Data presentation and encryption
Inter-host connection
End-to-end connections
Addresses and best path
Access to media
Binary transmission
Application
Presentation
Session
Transport
Network
Data Link
Physical
7
6
5
4
3
2
1
Layer 5: The Session Layer
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 34
Layer 5: The Session Layer
establishes, manages, and terminates sessions between communicating hosts
synchronizes dialog between presentation layer entities and manages their data exchange
offers provisions for efficient data transfer, class of service, and exception reporting of session, presentation, and application layer problems
manages data exchange between presentation layer entities

## Slide 35
Keywords: Common Format
User interface
Data presentation and encryption
Inter-host connection
End-to-end connections
Addresses and best path
Access to media
Binary transmission
Application
Presentation
Session
Transport
Network
Data Link
Physical
7
6
5
4
3
2
1
Layer6: The Presentation Layer
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 36
Layer6: The Presentation Layer
ensures that information sent by the application layer of one system is readable by the application layer of another system
translates between multiple data representation formats by using a common data representation format
concerned with data structures and negotiation of data transfer syntax
responsible for compression and encryption

## Slide 37
Keyword: Browser
User interface
Data presentation and encryption
Inter-host connection
End-to-end connections
Addresses and best path
Access to media
Binary transmission
Application
Presentation
Session
Transport
Network
Data Link
Physical
7
6
5
4
3
2
1
Layer 7: The Application Layer
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 38
Layer 7: The Application Layer
closest to the user
provides network services to user applications
does not provide services to any other OSI layer

## Slide 39: Protocols on ISO layers

## Slide 40
Data Encapsulation
5
4
3
2
1
5
4
3
2
1
H3
物 理 传 输 媒 体
数 据 部 分
数 据 部 分
数 据 部 分
数 据 部 分
10100110100101 比 特 流 10100110100101
T2
计算机 1
H5
H4
H2
首部
尾部
AP2
AP1
应 用 程 序 数 据
计算机 2
比特
帧
IP数据报
IP分组
TCP报文段
UDP报文段

## Slide 41
Peer-to-Peer Communications

## Slide 42: Computer Network & Network Reference Model
Overview of Computer Network
OSI Reference Model
TCP/IP Model
Network Topology
Network Devices

## Slide 43: The TCP/IP Model
The U.S. Department of Defense (DoD) created the TCP/IP reference model
The DoD wants its packets to get through every time, under any conditions, from any one point to any other point.
It brought about the creation of the TCP/IP model
TCP/IP model has since become the standard on which the Internet has grown

## Slide 44
The TCP/IP model has only four layers.
The TCP/IP Model
Application
Transport
Internet
Network Access

## Slide 45: The TCP/IP Model - Application Layer
Handles high-level protocols, issues of representation, encoding, and session control
TCP/IP combines all application-related issues into one layer, and assures this data is properly packaged for the next layer.

## Slide 46
The TCP/IP Model - Transport Layer
Deals with the quality-of-service issues of reliability, flow control, and error correction.
  Transmission Control Protocol (TCP)
  User Datagram Protocol(UDP)
  It package application layer information into units called segments

## Slide 47
The TCP/IP Model - Internet Layer
Purpose: Send source packets from any network on the internetwork and have them arrive at the destination independent of the path and networks
Best path determination and packet switching occur at this layer
Internet protocol (IP)

## Slide 48
The TCP/IP Model – Network Access Layer
Is also called the host-to-network layer.
It is concerned with all of the issues that an IP packet requires to actually make a physical link, and then to make another physical link.
It includes the LAN and WAN technology details, and all the details in the OSI physical and data link layers.

## Slide 49
Common TCP/IP Protocols
Application Layer
Transport Layer
Internet Layer
Network Access Layer

## Slide 50
FTP - File Transfer Protocol
HTTP - Hypertext Transfer Protocol
SMTP - Simple Mail Transfer protocol
DNS - Domain Name System
TFTP - Trivial File Transfer Protocol
Common TCP/IP Protocols

## Slide 51
both have layers, networking professionals need to know both
both have application layers, though they include very different services
both have comparable transport and network layers
packet-switched (not circuit-switched) technology is assumed
Similarities of TCP/IP and OSI
Application
Transport
Internet
Network Access
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 52
TCP/IP appears simpler because it has fewer layers
TCP/IP protocols are the standards around which the Internet developed, so the TCP/IP model gains credibility just because of its protocols.
Typically networks aren't built on the OSI protocol, even though the OSI model is used as a guide.
Differences of TCP/IP and OSI
Application
Transport
Internet
Network Access
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 53: Computer Network & Network Reference Model
Overview of Computer Network
OSI Reference Model
TCP/IP Model
Network Topology
Network Devices

## Slide 54
Topology
Defines the structure of the network
Physical topology: the actual layout of the wire (media)
  bus, star, ring, extended star, hierarchical, mesh
Logical topology: defines how the media is accessed by the hosts
  token passing

## Slide 55
Network Topologies

## Slide 56
Network Topologies--Bus
Physical Perspective Each host is wired to a common wire.
  Advantage: all hosts can communicate directly.
  Disadvantage: A break in the cable disconnects hosts from each other.
Logical Perspective
  Every networking device to see all signals from all other devices (advantage?)

## Slide 57
Network Topologies--Ring
Physical Perspective
  All devices wired directly to each other in what is called a daisy-chain.
Logical Perspective
  In order for information to flow, each station must pass the information to its adjacent station.

## Slide 58
Network Topologies — Dual Ring
Physical Perspective
  A dual ring topology is the same as a ring topology, except that there is a second, redundant ring, that connects the same devices.
  Advantages: provide reliability and flexibility
Logical Perspective
  A dual ring topology acts like two independent rings, of which, only one at a time is used.

## Slide 59
Network Topologies—Star
Physical Perspective A star topology has a central node with all links radiating from it.
  Advantage: it allows all other nodes to communicate with each other, conveniently. It also might be desirable for security or restricted access reasons
  disadvantage: if the central node fails, the whole network becomes disconnected. Depending on the type of networking device used, collisions can be a problem.
Logical Perspective The flow of all information would go through one device.

## Slide 60
Network Topologies—Tree
The tree topology uses a trunk node from which it branches to other nodes.
  binary tree (each node splits into two links)
  backbone tree (a backbone trunk has branch nodes with links hanging from it).
Physical Perspective The trunk is a wire that has several layers of branches.
Logical Perspective The flow of information is hierarchical.

## Slide 61
Network Topologies—
Complete (Mesh)
Physical Perspective
  has distinct advantages and disadvantages
    Advantage: the maximum connectivity and reliability.
    Disadvantage: the amount of media for the links, and the amount of connections to the links becomes overwhelming.
Logical Perspective
  The behavior of a complete, or mesh topology depends greatly on the devices used.

## Slide 62
Network Topologies—Cellular
Physical Perspective
  The cellular topology is for wireless technology
  Sometimes the receiving nodes move (e.g. cell phone), and sometimes the sending nodes move (e.g. satellite)
Logical Perspective
  Nodes communicate with each other directly (though sometimes extremely difficult), or communicate only with their adjacent cells, which is extremely inefficient.

## Slide 63: Computer Network & Reference Model
Overview of Computer Network
OSI Reference Model
TCP/IP Model
Network Topology
Network Devices

## Slide 64: LAN Devices in a Topology
Hosts—devices connected directly to network segment
  printers, computers, servers, FAX, copier
Hosts—not part of any layer, but the functions of the OSI model are performed in software inside host

## Slide 65
LAN Devices in a Topology

## Slide 66: NICs – Layer 2
Carries a unique code called a MAC address
Is used to control data communication for the host on the network
Translates parallel signal produced by computer into serial format to send over the network
Transceiver used to convert signals as well as send and receive bits
Provides the host’s access to the medium
至局域网
串行通信
硬件地址
适配器
（网卡）
CPU 和
存储器
生成发送的数据
处理收到的数据
把帧发送到局域网
从局域网接收帧
计算机
IP 地址
并行
通信

## Slide 67
NICs – Layer 2

## Slide 68
Media – Layer 1
Carries a flow of information in bits
The means by which signals travel from one networked device to another

## Slide 69
Repeaters – Layer 1
regenerate (amplify) and retime network signals at the bit level to allow them to travel a longer distance on the media
perform no filtering
used to extend the length of the network
clean, amplify, and resend signals that are weakened by long cable

## Slide 70
Hubs – Layer 1
used to regenerate and retime network signals
propagate signals
cannot filter traffic
cannot determine the best path
used as network concentration points
sometimes called multiport repeaters

## Slide 71
Repeaters/Hubs - Differences
Repeater typically has only two ports and a hub generally has from four to twenty or more ports.
Repeater receives on one port and repeats on the other, while hubs receive on one port and transmit on all other ports.
Hubs most commonly found in Ethernet 10Base T or 100Base T networks.

## Slide 72
Hub

## Slide 73
Bridges – Layer 2
purpose is to filter traffic on a LAN—to keep traffic local—yet allow connectivity to other segments of the LAN for traffic that is directed there
keep track of MAC addresses that are on each side of the bridge and make decisions based on this MAC address list
more intelligent than hubs
collect and pass packets between segments
create collision domains
maintain address tables

## Slide 75
Switches – Layer 2
used to concentrate connectivity
combine the connectivity of a hub with the traffic regulation of a bridge
switch frames from incoming ports to outgoing ports providing each port with full bandwidth
provide separate data paths

## Slide 76
Routers – Layer 3
important traffic-regulating device in large networks
Make decisions based on network addresses
examine packets (Layer 3 data), choose the best path for them, and then switch them out the proper outgoing port
two primary purposes: path selection and switching of packets to best route

## Slide 77
Clouds – Layers 1-7
all the devices that connect your computer to some very distant com-puter, perhaps on another continent
contain NICs, switches, bridges, routers, gateways, and other net-working devices

## Slide 78
Evolution of Networking Devices and the OSI Layers

## Slide 79
Evolution of Networking Devices and the OSI Layers
hosts and servers operate at Layers 1 – 7; they perform the encapsulation process
transceivers, repeaters, and hubs are all considered active Layer 1 devices because they act only on bits and require energy
patch cables, patch panels, and other interconnection components are considered passive Layer 1 components because they simply provide some sort of conducting path

## Slide 80
Evolution of Networking Devices and the OSI Layers
NICs are Layer 2 devices because they are the location of the MAC address; but because they often handle signaling and encoding, they are also Layer 1 devices.
Bridges and switches are Layer 2 devices because they use Layer 2 information to make decisions about whether to forward packets.
Routers are Layer 3 devices because they use Layer 3 addresses to choose best paths and to switch packets to proper route.

## Slide 81
Packet Flow Through Clouds
NICs
Switches
Bridges
Routers
Gateways (protocol transformation)
PCs (all devices that operate at all levels of the OSI model)

## Slide 82
谢 谢！