## Slide 1: OSI Layer 4: Transport Layer

## Slide 2: OSI Layer 4: Transport Layer
An overview of layer 4
TCP (Transmission Control Protocol)
UDP(User Datagram Protocol)
An application: NAT and PAT

## Slide 3: OSI Layer 4: Transport Layer
Layer 4 performs multiple functions:
    segmenting upper-layer application data
    establishing end-to-end operations
    sending segments from one end host to another
    Flow control and reliability
      can be compared to talking to a foreigner.
      Often you would ask the foreigner to repeat his/her words (reliability) and to speak slowly (flow control)

## Slide 4: Layer 4: The Transport Layer
Two particularly important Layer 4 protocols:
  Transmission Control Protocol (TCP)
  User Datagram Protocol (UDP)

## Slide 5: Layer 4: The Transport Layer
    Divide outgoing messages into segments
    Reassemble messages at the destination station
TCP : reliable
  Connection -oriented
  Software checking for segment
  Re-send anything lost or error
  Uses acknowledgments
  Provides flow control
UDP: unreliable
  connectionless
  provides no software checking for segment
  uses no acknowledgments
  provides no flow control

## Slide 6: Service Model
Both TCP and UDP use port to keep track of different conversations that cross the network at the same time
Application software developers have agreed to use the well-known port numbers that are defined in RFC1700
Port numbers below 255 are reserved for TCP and UDP public applications.

## Slide 7
    Socket is presented as (IP_address, port)
    Every connection is expressed as (socketsource, socketdestination), which is a point-to-point full-duplex channel
    Does not support multicast and broadcast
Socket

## Slide 8: Layer 4: The Transport Layer
An overview of layer 4
TCP (Transmission Control Protocol)
UDP(User Datagram Protocol)
An application: NAT and PAT

## Slide 9: TCP Service Model
Problems must be solved in TCP:
  Reliable transfer
  Flow control
    Sliding window
    congestion avoidance…
  Connection management
    Establish connection：three handshakes
    Release connection： four handshakes

## Slide 10
TCP
首部
20
字节
固定
首部
目 的 端 口
数据
偏移
检 验 和
选 项 （长 度 可 变）
源 端 口
序 号
紧 急 指 针
窗 口
确 认 号
保 留
F
I
N
S
Y
N
R
S
T
P
S
H
A
C
K
U
R
G
位 0 8 16 24 31
填 充
源端口和目的端口字段——各占 2 字节
端口是运输层与应用层的服务接口
运输层的复用和分用功能都要通过端口才能实现

## Slide 11
TCP
首部
20
字节
固定
首部
目 的 端 口
数据
偏移
检 验 和
选 项 （长 度 可 变）
源 端 口
序 号
紧 急 指 针
窗 口
确 认 号
保 留
F
I
N
S
Y
N
R
S
T
P
S
H
A
C
K
U
R
G
位 0 8 16 24 31
填 充
序号字段——占 4 字节
TCP 传送的数据流中的每一个字节都编上一个序号
序号字段的值指本报文段所发送的数据的第一个字节的序号

## Slide 12
TCP
首部
20
字节
固定
首部
目 的 端 口
数据
偏移
检 验 和
选 项 （长 度 可 变）
源 端 口
序 号
紧 急 指 针
窗 口
确 认 号
保 留
F
I
N
S
Y
N
R
S
T
P
S
H
A
C
K
U
R
G
位 0 8 16 24 31
填 充
确认号字段——占 4 字节，是期望收到对方的下一个报文段的数据的第一个字节的序号

## Slide 13
TCP
首部
20
字节
固定
首部
目 的 端 口
数据
偏移
检 验 和
选 项 （长 度 可 变）
源 端 口
序 号
紧 急 指 针
窗 口
确 认 号
保 留
F
I
N
S
Y
N
R
S
T
P
S
H
A
C
K
U
R
G
位 0 8 16 24 31
填 充
数据偏移（即首部长度）——占 4 位
指出 TCP 报文段的数据起始处距TCP 报文段的起始处的长度
单位是 32 位字（以 4 字节为计算单位）

## Slide 14
TCP
首部
20
字节
固定
首部
目 的 端 口
数据
偏移
检 验 和
选 项 （长 度 可 变）
源 端 口
序 号
紧 急 指 针
窗 口
确 认 号
保 留
F
I
N
S
Y
N
R
S
T
P
S
H
A
C
K
U
R
G
位 0 8 16 24 31
填 充
保留字段——占 6 位，保留为今后使用，目前置 0

## Slide 15
TCP
首部
20
字节
固定
首部
目 的 端 口
数据
偏移
检 验 和
选 项 （长 度 可 变）
源 端 口
序 号
紧 急 指 针
窗 口
确 认 号
保 留
F
I
N
S
Y
N
R
S
T
P
S
H
A
C
K
U
R
G
位 0 8 16 24 31
填 充
紧急 URG  1 时，表明紧急指针字段有效
告诉系统此报文段中有紧急数据，应尽快传送(相当于高优先级的数据)

## Slide 16
TCP
首部
20
字节
固定
首部
目 的 端 口
数据
偏移
检 验 和
选 项 （长 度 可 变）
源 端 口
序 号
紧 急 指 针
窗 口
确 认 号
保 留
F
I
N
S
Y
N
R
S
T
P
S
H
A
C
K
U
R
G
位 0 8 16 24 31
填 充
ACK  1 时确认号字段有效
ACK  0 时确认号字段无效

## Slide 17
TCP
首部
20
字节
固定
首部
目 的 端 口
数据
偏移
检 验 和
选 项 （长 度 可 变）
源 端 口
序 号
紧 急 指 针
窗 口
确 认 号
保 留
F
I
N
S
Y
N
R
S
T
P
S
H
A
C
K
U
R
G
位 0 8 16 24 31
填 充
推送 PSH (PuSH) —— 接收 TCP 收到 PSH = 1 的报文段，就尽快地交付接收应用进程，而不再等到整个缓存都填满了后再向上交付

## Slide 18
TCP
首部
20
字节
固定
首部
目 的 端 口
数据
偏移
检 验 和
选 项 （长 度 可 变）
源 端 口
序 号
紧 急 指 针
窗 口
确 认 号
保 留
F
I
N
S
Y
N
R
S
T
P
S
H
A
C
K
U
R
G
位 0 8 16 24 31
填 充
复位 RST (ReSeT 1 时，表明 TCP 连接中出现严重差错（如由于主机崩溃或其他原因），必须释放连接，然后再重新建立运输连接

## Slide 19
TCP
首部
20
字节
固定
首部
目 的 端 口
数据
偏移
检 验 和
选 项 （长 度 可 变）
源 端 口
序 号
紧 急 指 针
窗 口
确 认 号
保 留
F
I
N
S
Y
N
R
S
T
P
S
H
A
C
K
U
R
G
位 0 8 16 24 31
填 充
同步 SYN=1 表示这是一个连接请求或连接接受报文

## Slide 20
TCP
首部
20
字节
固定
首部
目 的 端 口
数据
偏移
检 验 和
选 项 （长 度 可 变）
源 端 口
序 号
紧 急 指 针
窗 口
确 认 号
保 留
F
I
N
S
Y
N
R
S
T
P
S
H
A
C
K
U
R
G
位 0 8 16 24 31
填 充
终止 FIN (FINis) —— 用来释放一个连接。FIN  1 表明此报文段的发送端的数据已发送完毕，并要求释放运输连接。

## Slide 21: 窗口字段 —— 占 2 字节，用来让对方设置发送窗口的依据，单位为字节。
TCP
首部
20
字节
固定
首部
目 的 端 口
数据
偏移
检 验 和
选 项 （长 度 可 变）
源 端 口
序 号
紧 急 指 针
窗 口
确 认 号
保 留
F
I
N
S
Y
N
R
S
T
P
S
H
A
C
K
U
R
G
位 0 8 16 24 31
填 充

## Slide 22
TCP
首部
20
字节
固定
首部
目 的 端 口
数据
偏移
检 验 和
选 项 （长 度 可 变）
源 端 口
序 号
紧 急 指 针
窗 口
确 认 号
保 留
F
I
N
S
Y
N
R
S
T
P
S
H
A
C
K
U
R
G
位 0 8 16 24 31
填 充
检验和 —— 占 2 字节。检验和字段检验的范围包括首部和数据这两部分

## Slide 23
TCP
首部
20
字节
固定
首部
目 的 端 口
数据
偏移
检 验 和
选 项 （长 度 可 变）
源 端 口
序 号
紧 急 指 针
窗 口
确 认 号
保 留
F
I
N
S
Y
N
R
S
T
P
S
H
A
C
K
U
R
G
位 0 8 16 24 31
填 充
紧急指针字段 —— 占 16 位，指出在本报文段中紧急数据共有多少个字节（紧急数据放在本报文段数据的最前面）

## Slide 24
TCP
首部
20
字节
固定
首部
目 的 端 口
数据
偏移
检 验 和
选 项 （长 度 可 变）
源 端 口
序 号
紧 急 指 针
窗 口
确 认 号
保 留
F
I
N
S
Y
N
R
S
T
P
S
H
A
C
K
U
R
G
比特 0 8 16 24 31
填 充
TCP 最初只有一种选项，即最大报文段长度 MSS(Maximum Segment Size)
MSS 告诉对方缓存所能接收的报文段的数据字段的最大长度是 MSS 个字节
数据字段加上 TCP 首部才等于整个的 TCP 报文段
。

## Slide 25
TCP
首部
20
字节
固定
首部
目 的 端 口
数据
偏移
检 验 和
选 项 （长 度 可 变）
源 端 口
序 号
紧 急 指 针
窗 口
确 认 号
保 留
F
I
N
S
Y
N
R
S
T
P
S
H
A
C
K
U
R
G
位 0 8 16 24 31
填 充
填充字段 —— 这是为了使整个首部长度是 4 字节的整数倍。

## Slide 26: TCP Protocol
Hosts exchange data by using segment(TPDU)
Each segment has:
  a header of 20 bytes(except optional parts)
  0 or more data bytes
The size of the segment must be matched with IP packets, and also must satisfy the demand of bottom layers
  For example, the MTU(Maximal Transfer Unit) of Ethernet is 1500 bytes
Each byte has a 32 bits sequence number

## Slide 27: Reliable Connection?
Two-army Problem

## Slide 28: TCP: Establish Connection
SYN = 1, seq = x
Closed
Closed
Active open
Passive
open
A
B
Client
Server
The First Handshake
  Server: executes LISTEN and ACCEPT primitive, and monitors passively
  Client: executes CONNECT primitive, generate a TCP segment with SYN=1 and ACK=0,which stands for connection request

## Slide 29: TCP: Establish Connection
SYN = 1, seq = x
SYN = 1, ACK = 1, seq = y, ack= x  1
The Second Handshake
  Server checks if exists service process monitoring the port
    If none process, answer a TCP segment with RST=1
    If exists process, decides to reject or to accept the request
    If accept the connection request, send a segment with SYN=1 and ACK=1
Closed
Closed
Active open
Passive
open
A
B
Client
Server

## Slide 30: TCP: Establish Connection
SYN = 1, seq = x
ACK = 1, seq = x + 1, ack = y  1
SYN = 1, ACK = 1, seq = y, ack= x  1
  The Third Handshake
    The client sends a segment with SYN=0 and ACK=1 to acknowledge the connection
Closed
Closed
Active open
Passive
open
A
B
Client
Server

## Slide 31: TCP: Establish Connection
SYN = 1, seq = x
ACK = 1, seq = x + 1, ack = y  1
Data Transfer
SYN = 1, ACK = 1, seq = y, ack= x  1
When the server receives the acknowledgement, it informs the upper layer applications
Closed
Closed
Active open
Passive
open
A
B
Client
Server

## Slide 32
SYN-
SENT
ESTAB-
LISHED
SYN-
RCVD
LISTEN
ESTAB-
LISHED
SYN = 1, seq = x
ACK = 1, seq = x + 1, ack = y  1
Data Transfer
SYN = 1, ACK = 1, seq = y, ack= x  1
TCP: Establish Connection
Closed
Closed
Active open
Passive
open
A
B
Client
Server

## Slide 33: Example: Establish Connection
TCP A TCP B
1. CLOSED LISTEN
2. SYN-SENT --> <SEQ=100><CTL=SYN> --> SYN-RECEIVED
3. ESTABLISHED <-- <SEQ=300><ACK=101><CTL=SYN,ACK> <-- SYN-RECEIVED
4. ESTABLISHED --> <SEQ=101><ACK=301><CTL=ACK> --> ESTABLISHED
5. ESTABLISHED --> <SEQ=101><ACK=301><CTL=ACK><DATA> --> ESTABLISHED
Basic 3-Way Handshake for Connection Synchronization
Note that the ACK does not occupy sequence number space (if it did, we would wind up ACKing ACK's!)

## Slide 34: Data transfer ——stop-and-wait protocol
(a) No error
A
Send M1
ACK M1
B
Send M2
Send M3
ACK M2
ACK M3
A
Send M1
B
Resend M1
Send M2
ACK M1
Dispose
the segment

(b) Out of time
t
t
t
t

## Slide 35: Data transfer ——stop-and-wait protocol
After sending a segment, preserve a backup temporarily
Each segment and ACK must have ID
The resend-time must be more than average-travel-time *2
stop-and-wait protocol is a simple protocol, but has poor efficiency

## Slide 36: Data transfer ——Lost ACK and Late ACK
A
Send M1
B
Out of time
Resend M1
Send M2
Dispose the repeated M1 and resend ACKM2

(a) Lost ACK
ACK M1
A
Send M1
B
Out of time
Resend M1
Send M2
Dispose the repeated M1 and resend ACKM1

(b) Late ACK
ACK M1
Receive the
late ACK and
do nothing
t
t
t
t

## Slide 37: Reliable Communication
ARQ (Automatic Repeat reQuest)。
  It means the ‘resend request’ is automatically sent and the receiver need not request the sender to resend the error segment

## Slide 38: Contiguous ARQ Protocol
1
2
3
4
5
6
7
8
9
10
11
12
(a) 发送方维持发送窗口（发送窗口是 5）
发送窗口
(b) 收到一个确认后发送窗口向前滑动
向前
1
2
3
4
5
6
7
8
9
10
11
12
发送窗口
Segment
t
t
ACK

## Slide 39
FIN = 1, seq = u
ESTAB-
LISHED
CLOSED
Data Transfer
ESTAB-
LISHED
TCP: Release Connection
Active Close
Passive
Close
A
B
Client
Server

## Slide 40
FIN = 1, seq = u
ACK = 1, seq = v, ack= u  1
ESTAB-
LISHED
Data Transfer
ESTAB-
LISHED
Active Close
Inform Upper Layer
A
B
Client
Server
TCP: Release Connection

## Slide 41
FIN = 1, seq = u
ACK = 1, seq = v, ack= u  1
FIN = 1, ACK = 1, seq = w, ack= u  1
Passive
Close
Data Transfer
ESTAB-
LISHED
Data Transfer
ESTAB-
LISHED
Active Close
Inform Upper Layer
A
B
Client
Server
TCP: Release Connection

## Slide 42
FIN = 1, seq = u
ACK = 1, seq = v, ack= u  1
FIN = 1, ACK = 1, seq = w, ack= u  1
ACK = 1, seq = u + 1, ack = w  1
TCP: Release Connection
Passive
Close
Data Transfer
ESTAB-
LISHED
Data Transfer
ESTAB-
LISHED
Active Close
Inform Upper Layer
A
B
Client
Server

## Slide 43
CLOSED
ACK = 1, seq = u + 1, ack = w  1
FIN = 1, seq = u
ACK = 1, seq = v, ack= u  1
FIN = 1, ACK = 1, seq = w, ack= u  1
FIN-
WAIT-1
CLOSE-
WAIT
FIN-
WAIT-2
LAST-
ACK
Wait 2MSL
TIME-
WAIT

CLOSED
Before releasing connection, the client must wait for 2MSL
TCP: Release Connection
Passive
Close
Data Transfer
ESTAB-
LISHED
Data Transfer
ESTAB-
LISHED
Active Close
Inform Upper Layer
A
B
Client
Server

## Slide 44: Why must wait for 2MSL?
To ensure the last ACK sent by A can reach B
To prevent any invalid connection request segment from emerging
  After waiting for 2MSL , we can make sure that all segments on the connection have disappeared

## Slide 45: T C P 的 有 限 状 态 机
CLOSED
ESTABLISHED
LISTEN
CLOSE_WAIT
FIN_WAIT_1
SYN_RCVD
FIN_WAIT_2
CLOSING
TIME_WAIT
SYN_SENT
LAST_ACK
主动打开
被动打开
被动关闭
主动关闭
起点
被动打开
主动打开
发送 SYN
同时打开
收到 SYN，发送 SYN, ACK
收到 ACK
数据传送
阶段
关闭
发送 FIN
关闭
发送 FIN
关闭
发送 FIN
收到 RST
收到 SYN
发送 SYN, ACK
关闭
或超时
收到 ACK
收到 SYN, ACK
发送 ACK
收到 ACK
收到 ACK
收到 FIN
发送 ACK
收到 FIN, ACK
发送 ACK
收到 FIN
发送 ACK
同时关闭
收到 FIN
发送 ACK
发送 SYN
定时经过两倍报文段寿命后
关闭

## Slide 46: Layer 4: The Transport Layer
An Overview of Layer 4
TCP (Transmission Control Protocol)
UDP(User Datagram Protocol)
An application: NAT and PAT

## Slide 47: UDP (User Datagram Protocol)
Why do we need UDP?
  No connection establishment (which can add delay)
  Simple: no connection state at sender, receiver
  Small segment header
  No congestion control: UDP can blast away as fast as desired

## Slide 48: UDP (User Datagram Protocol)
Connectionless:
  no handshaking between UDP sender, receiver
  each UDP segment handled independently of others
Often used for streaming multimedia applications
  loss tolerant
  rate sensitive
UDP are used in:
  RIP: To send the route information periodically
  DNS: Avoid the delay to setup the TCP connection
  SNMP: When congestion, SNMP must still runable. Without the congestion and reliability control mechanism, UDP has better performance than TCP under the circumstances.
  Other protocols include TFTP, DHCP
Add reliability at application layer if necessary

## Slide 49: UDP (User Datagram Protocol)

## Slide 51: Layer 4: The Transport Layer
An Overview of Layer 4
TCP (Transmission Control Protocol)
UDP(User Datagram Protocol)
An application: NAT and PAT

## Slide 52
NAT, is the process of swapping one address for another in the IP packet header
In practice, NAT is used to allow hosts that are privately addressed to access the Internet
One of solutions to IP address depletion
  Conserves registered (legal) addresses
  Increases Flexibility when connecting to Internet
RFC 1631 - Network Address Translator (NAT)
What is NAT?
Notes: Because many private networks exist alongside public nets, grabbing "just any address" is strongly discouraged. RFC 1918 sets aside three blocks of IP addresses (i.e., a Class A, a Class B, and a Class C range) for private, internal use. Addresses in this range will not be routed on the Internet backbone . Internet routers immediately discard private addresses. When using private addresses on a network that is connected to the Internet, you should filter packets and routing updates to avoid "leaking" any RFC 1918 addresses between autonomous systems. For example, if both you and your provider use addresses from the 192.168.0.0 /16 block, your routers could get confused if confronted with updates from both systems.
NAT is the process of swapping one address for another in the IP packet header. In practice, NAT is used to allow hosts that are privately addressed (using RFC 1918 addresses) to access the Internet.
When a host inside the private domain wants to transmit to a host on the outside world, it forwards the packet to the NAT-enabled device. The NAT process then looks inside the IP header and, if appropriate, replaces the inside IP address with a globally unique IP address. When an outside host sends a response, the NAT process receives it, checks the current table of network address translations, and replaces the destination address with the original inside source. NAT translations can occur dynamically or statically and can be used for a variety of purposes. The most powerful feature of NAT routers is their capability to use port address translation (PAT), which allows multiple inside addresses to map to the same global address. This is sometimes called a "many-to-one" NAT. This procedure allows for many user inside of the private network to share one single external IP address. When using PAT the NAT router keeps track of the different conversations by mapping TCP and UDP port numbers.

## Slide 53: NAT a simple concept
Private addresses
Registered addresses

## Slide 54: NAT types
Static NAT:
Fixed mapping of an internal address to an registered address
Dynamic NAT:
Mapping is done dynamically on a first come first served basis
PAT (Overload):
Port address translation is used to allow many internal users to share a single ‘inside global’ address

## Slide 55: NAT address types
Inside Local address (内部本地地址 ):内网IP地址
Inside Global address (内部全局地址): 注册IP地址,对外部展示的内部地址
Outside Global address (外部全局地址):由主机所有者分配的IP地址。通常是注册地址。

## Slide 56: NAT address types
10.1.1.2
10.1.1.1
NAT table
198.168.2.2
198.168.2.1
172.81.7.3
172.80.7.3
10.1.1.3
198.168.2.3
172.81.7.3
Internet
Inside
10.1.1.1
Host B
172.80.7.3
1
3
SA
10.1.1.1
DA
10.1.1.1
SA
198.168.2.1
DA
198.168.2.1
10.1.1.2
10.1.1.3
4
5
2
Host C
172.81.7.3
Inside Global IP
Address
Outside Global
IP Address
Inside Local IP
Address
Inside Local addresses
Outside Global addresses
Inside Global
addresses
Outside
Host A

## Slide 57: Static: How does it work?
Static
Translation Table
10.1.1.2 = 203.10.10.2 10.1.1.3 = 203.10.10.3 10.1.1.4 = 203.10.10.4
10.1.1.2
10.1.1.3
10.1.1.4
Inside
Outside
E0/0
S0/0

## Slide 58: Dynamic:How does it work?
Dynamic
Translation Table
10.1.1.4 = 203.10.10.2 10.1.1.2 = 203.10.10.3 10.1.1.3 = 203.10.10.4
10.1.1.2
10.1.1.3
10.1.1.4
Inside
Outside
E0/0
S0/0
Notes: access-list 2 permit 10.1.1.0 0.0.0.255

## Slide 59: Advantages and Disadvantages of NAT
Advantage: since not every inside host needs outside access at the same time, you can get away with using a small pool of globally unique addresses to serve a relatively large number of privately addressed hosts.
Disadvantage: one-to-one mapping.
That is, if the private address space is a /8, but the public address is a /24, only 254 hosts can access the Internet at a time.

## Slide 60: PAT: How does it work?
Port Translation Table
Inside Local IP SRC Port DST Port Inside Global IP
10.1.1.4 1024 80 203.10.10.2
10.1.1.2 1122 80 203.10.10.2
10.1.1.3 1343 80 203.10.10.2
10.1.1.2
10.1.1.3
10.1.1.4
Inside
Outside
E0/0
S0/0
Notes: access-list 2 permit 10.1.1.0 0.0.0.255
ip nat inside source list 101 interface dialer1 overload
access-list 101 permit ip 10.0.0.0 0.255.255.255 any

## Slide 61: PAT Operation
10.1.1.2:1723
10.1.1.1:1024
NAT table
198.168.2.2:1723
198.168.2.2:1024
172.81.7.3:23
172.80.7.3:23
TCP
TCP
10.1.1.3:1723
198.168.2.2:1492
172.81.7.3:23
TCP
Internet
Inside
10.1.1.1
Host B
172.80.7.3
1
3
SA
10.1.1.1
DA
10.1.1.1
SA
198.168.2.2
DA
198.168.2.2
10.1.1.2
10.1.1.3
4
2
Host C
172.81.7.3
DA
198.168.2.2
4
Inside Global IP
Address: Port
Outside Global
IP Address: Port
Protocol
Inside Local IP
Address: Port
Most common situation for small Networks.
Host A
5

## Slide 62
谢 谢！